## Slide 1
Chapter 1: Introduction to Computer
Architecture
Prof. Smruti Ranjan Sarangi
IIT Delhi
Basic Computer Architecture
PowerPoint Slides

## Slide 2
Download the pdf of the book
www.basiccomparch.com
videos
Slides, software, solution manual
Print version
(Publisher: WhiteFalcon, 2021)
Available on e-commerce sites.
The pdf version of the book and all the learning resources can be freely downloaded from the website: www.basiccomparch.com
2nd version

## Slide 3: What is Computer Architecture ?
Computer Architecture
  The view of a computer as presented to software designers
Computer Organization
  The actual implementation of a computer in hardware.
Answer : It is the study of computers ?
3

## Slide 4: What is a Computer ?
A computer is a general purpose device that can be programmed to process
information, and yield meaningful results.
4

## Slide 5: How does it work ?
Program – List of instructions given to the computer
Information store – data, images, files, videos
Computer – Process the information store according to the instructions in the program
Computer
Program
Information
store
results
5

## Slide 6: What does a computer look like ?
Let us take the lid off a desktop computer
CPU
Memory
Hard disk
6

## Slide 7
Memory – Stores programs and data. Gets destroyed when the computer is powered off
Hard disk – stores programs/data permanently
Computer
Memory
Hard disk
7

## Slide 8: Let us make it a full system ...
Computer
Memory
Hard disk
Keyboard
Mouse
Monitor
Printer
8

## Slide 9: Food for Thought...
What is the most intelligent computer ?
9

## Slide 10: Answer ...
Our brilliant brains
10

## Slide 11: Outline
Language of Instructions
  Instruction Set Architecture
  Features of an ISA – Complete, Concise, Generic, Simple
Completeness of an ISA
  Turing Machines
  Universal Machines
  Single Instruction/Multi-Instruction ISA
Design of Practical Machines
  Harvard/ Von Neumann Machines
  Registers
Road Ahead
11

## Slide 12: How does an Electronic Computer Differ from our Brain ?
Computers are ultra-fast and ultra-dumb
Feature
Computer
Our Brilliant Brain
Intelligence
Dumb
Intelligent
Speed of basic calculations
Ultra-fast
Slow
Can get tired
Never
After sometime
Can get bored
Never
Almost always
12

## Slide 13: How to Instruct a Computer ?
Write a program in a high level language – C, C++, Java
Compile it into a format that the computer understands
Execute the program
Program
Executable
Output
compile
execute
13

## Slide 14: What Can a Computer Understand ?
Computer can clearly NOT understand instructions of the form
  Multiply two matrices
  Compute the determinant of a matrix
  Find the shortest path between Mumbai and Delhi
They understand :
  Add a + b to get c
  Multiply a * b to get c
14

## Slide 15: The Language of Instructions
Humans can understand
  Complicated sentences
    English, French, Spanish
Computers can understand
  Very simple instructions
The semantics of all the instructions supported by a processor is known
as its instruction set architecture (ISA). This includes the semantics of
the instructions themselves, along with their operands, and interfaces
with peripheral devices.
15

## Slide 16: Features of an ISA
Example of instructions in an ISA
  Arithmetic instructions : add, sub, mul, div
  Logical instructions : and, or, not
  Data transfer/movement instructions
Complete
  It should be able to implement all the programs that users may write.
16

## Slide 17: Features of an ISA – II
Concise
  The instruction set should have a limited size. Typically an ISA contains 32-1000 instructions.
Generic
  Instructions should not be too specialized, e.g. add14 (adds a number with 14) instruction is too specialized
Simple
  Should not be very complicated.
17

## Slide 18: Designing an ISA
Important questions that need to be answered :
  How many instructions should we have ?
  What should they do ?
  How complicated should they be ?
Two different paradigms : RISC and CISC
RISC
(Reduced Instruction Set
Computer)
CISC
(Complex Instruction
Set Computer)
18

## Slide 19: RISC vs CISC
A reduced instruction set computer (RISC) implements
simple instructions that have a simple and regular
structure. The number of instructions is typically a small
number (64 to 128). Examples: ARM, IBM PowerPC,
HP PA-RISC
A complex instruction set computer (CISC) implements complex instructions that are highly irregular, take multiple operands, and implement complex functionalities. Secondly, the number of instructions is large (typically
500+). Examples: Intel x86, VAX
19

## Slide 20: Summary Uptil Now ...
Computers are dumb yet ultra-fast machines.
Instructions are basic rudimentary commands used to communicate with the processor. A computer can execute billions of instructions per second.
The compiler transforms a user program written in a high level language such as C to a program consisting of basic machine instructions.
The instruction set architecture(ISA) refers to the semantics of all the instructions supported by a processor.
The instruction set needs to be complete. It is desirable if it is also concise, generic, and simple.
20

## Slide 21: Outline
Language of Instructions
  Instruction Set Architecture
  Features of an ISA – Complete, Concise, Generic, Simple
Completeness of an ISA
  Turing Machines
  Universal Machines
  Single Instruction/Multi-Instruction ISA
Design of Practical Machines
  Harvard/ Von Neumann Machines
  Registers
Road Ahead
21

## Slide 22: Completeness of an ISA
Complete means :
  Can implement all types of programs
  For example, if we just have add instructions, we cannot subtract (NOT Complete)
How can we ensure that an
ISA is complete ?
22

## Slide 23: Completeness of an ISA – II
How to ensure that we have just enough instructions such that we can implement every possible program that we might want to write ?
23
Skip this part

## Slide 24: Answer
Let us look at results in theoretical computer science
Is there an universal ISA ?
Universal ISA
Universal Machine
The universal machine has a set of basic actions, and each such
action can be interpreted as an instruction.
24

## Slide 25: The Turing Machine – Alan Turing
Facts about Alan Turing
  Known as the father of computer science
  Discovered the Turing machine that is the most powerful computing device known to man
  Indian connection : His father worked with the Indian Civil Service at the time he was born. He was posted in Chhatrapur, Odisha.
25

## Slide 26: Turing Machine
Infinite Tape
State Register
Tape Head
L
R
Action Table
(old state, old symbol) -> (new state, new symbol, left/right)
26
The tape head can only move left or right

## Slide 27: Operation of a Turing Machine
There is an inifinite tape that extends to the left and right. It consists of an infinite number of cells.
The tape head points to a cell, and can either move 1 cell to the left or right
Based on the symbol in the cell, and its current state, the Turing machine computes the transition :
  Computes the next state
  Overwrites the symbol in the cell (or keeps it the same)
  Moves to the left or right by 1 cell
The action table records the rules for the transitions.
27

## Slide 28: Example of a Turing Machine
Start from the rightmost position. (state = 1)
If (state = 1), replace a number x, by x+1 mod 10
The new state is equal to the value of the carry
Keep going left till the '$' sign
Design a Turing machine to increment a number by 1.
Tape Head
$
3 4 6 9
$
7
28

## Slide 29: More about the Turing Machine
This machine is extremely simple, and extremely powerful
  We can solve all kinds of problems – mathematical problems, engineering analyses, protein folding, computer games, …
  Try to use the Turing machine to solve many more types of problems (TODO)
29

## Slide 30: Church-Turing Thesis
Note : It is a thesis, not a theorem
For the last 60 years, nobody has found a counter-example
Church-Turing thesis: Any real-world computation can be translated
into an equivalent computation involving a Turing machine.
(source: Wolfram Mathworld)
Any computing system that is equivalent to a Turing machine is said to be
Turing complete.
Definition:
30

## Slide 31: Universal Turing Machine
For every problem in the world, we can design a Turing Machine (Church-Turing thesis)
Can we design a universal Turing machine that can simulate any Turing machine. This will make it a universal machine (UTM)
Why not? The logic of a Turing machine is really simple. We need to move the tape head left, or right, and update the symbol and state based on the action table. A UTM can easily do this.
A UTM needs to have an action table, state register, and tape that can simulate any arbitrary Turing machine.
31

## Slide 32: Universal Turing Machine
Prog. 1
Prog. 2
Prog. 3
Turing Machine 1
Turing Machine 2
Turing Machine 3
Universal Turing Machine
32

## Slide 33: A Universal Turing Machine
Generic State Register
Tape Head
L
R
Generic Action Table
Simulated Action Table
Simulated State Register
Work Area
33

## Slide 34
Generic State Register
Tape Head
L
R
Generic Action Table
Simulated Action Table
Simulated State Register
Work Area
A Universal Turing Machine - II
CPU
Data Memory
Instruction Memory
Program Counter
(PC)
Program
PC

## Slide 35: Computer Inspired from the Turing Machine
CPU
Program
Counter (PC)
Program
Data
Memory
Control
Unit
Arithmetic
Unit
Instruction
35
Program

## Slide 36: Elements of a Computer
Memory (array of bytes) contains
  The program, which is a sequence of instructions
  The program data → variables, and constants
The program counter(PC) points to an instruction in a program
  After executing an instruction, it points to the next instruction by default
  A branch instruction makes the PC point to another instruction (not in sequence)
CPU (Central Processing Unit) contains the
  Program counter, instruction execution units
36

## Slide 37: Let us now design an ISA ...
Single Instruction ISA
  sbn – subtract and branch if negative
Add (a + b) (assume temp = 0)
1: sbn temp, b, 2
2: sbn a, temp, exit
37

## Slide 38: Single Instruction ISA - II
Add the numbers – 1 … 10
1: sbn temp, temp, 2 // temp = 0
2: sbn temp, index, 3 // temp = -1 * index
3: sbn sum, temp, 4 // sum += index
4: sbn index, one, exit // index -= 1
5: sbn temp, temp, 6 // temp = 0
6: sbn temp, one, 1 // (0 - 1 < 0), hence goto 1
Initialization:
one = 1
index = 10
sum = 0
exit
38

## Slide 39: Multiple Instruction ISA
Arithmetic Instructions
  add, subtract, multiply, divide
Logical Instructions
  or, and, not
Move instructions
  Transfer values between memory locations
Branch instructions
  Move to a new program location, based on the values of some memory locations
39

## Slide 40: Outline
Language of Instructions
  Instruction Set Architecture
  Features of an ISA – Complete, Concise, Generic, Simple
Completeness of an ISA
  Turing Machines
  Universal Machines
  Single Instruction/Multi-Instruction ISA
Design of Practical Machines
  Harvard/ Von Neumann Machines
  Registers
Road Ahead
40

## Slide 41: Designing Practical Machines
Harvard Architecture
CPU
Control
ALU
Instruction
memory
Data
memory
I/O devices
41

## Slide 42: Von-Neumann Architecture
CPU
Control
ALU
Memory
I/O devices
42

## Slide 43: Problems with Harvard/ Von-Neumann Architectures
The memory is assumed to be one large array of bytes
  It is very very slow
  Solution:
    Have a small array of named locations (registers) that can be used by instructions
    This small array is very fast
General Rule: Larger is a structure, slower it is
Insight: Accesses exhibit locality (tend to use the same
variables frequently in the same window of time)
43

## Slide 44: Uses of Registers
A CPU (Processor) contains set of registers (16-64)
These are named storage locations.
Typically values are loaded from memory to registers.
Arithmetic/logical instructions use registers as input operands
Finally, data is stored back into their memory locations.
44

## Slide 45: Example of a Program in Machine Language with Registers
r1, r2, and r3, are registers
mem → array of bytes representing memory
1: r1 = mem[b] // load b
2: r2 = mem[c] // load c
3: r3 = r1 + r2 // add b and c
4: mem[a] = r3 // save the result
45

## Slide 46: Machine with Registers
CPU
Control
ALU
Memory
I/O devices
Registers
46

## Slide 47: Outline
Language of Instructions
  Instruction Set Architecture
  Features of an ISA – Complete, Concise, Generic, Simple
Completeness of an ISA
  Turing Machines
  Universal Machines
  Single Instruction/Multi-Instruction ISA
Design of Practical Machines
  Harvard/ Von Neumann Machines
  Registers
Road Ahead
47

## Slide 48: Where are we ...
We have derived the structure of a computer from theoretical fundamentals.
It has a CPU with a program counter & registers, memory, and peripherals.
The Instruction Set Architecture (ISA) is the link between hardware and software.
Instruction
Set
Architecture
48

## Slide 49: Instruction Set Architecture
Interface between software and hardware
  A compiler converts a program into machine instructions in the given ISA
  The processor executes the instructions in the ISA
We shall first look at the software aspect of the ISA (assembly programs)
Then look at implementing the ISA by designing the processor
Then, we shall make the computer more efficient by designing fast memory/ storage systems
At the end, we will look at multiprocessors
49

## Slide 50: Roadmap of the Course
Software
engineer
Hardware
designer
Language
of bits
ARM assembly
x86 assembly
Assembly
language
Software interface
Instruction set architecture
Processor Design
Building blocks:
gates, registers,
and memories
2
Computer
arithmetic
Processor
design
3
5
4
6
7
8
System design
Design of a simple processor
Memory
system
10
I/O and storage
12
Multiprocessors
11
Hardware
designer
Pipelining
9
50

## Slide 51
THE END
51