## Slide 1: NanoTHERM: A FOURIER-BOLTZmann framework for full chip thermal simulations
Shashank Varshney+, hameedah sultan+, palkesh jain*. Smruti Ranjan Sarangi+
* Department of Computer Science and Engineering IIT Delhi, India + Qualcomm India

## Slide 2: Motivation
Existing simulators’ problems
Need of thermal simulators
To enable thermal aware design
To compute leakage power
To reduce design time
To capture self heating
  FEM or FDM based
  Slow
  Mesh sensitive
  Ignore quantum effects
3

## Slide 3: Background
Finite Difference
𝜌𝑐_𝑝 𝜕𝑇/𝜕𝑡= 𝛻∙(κ𝛻𝑇)+𝑞 ̇
Green’s function
Impulse response of a unit power source
𝑇=𝐺 ⊛ 𝑃
Fourier heat equation
Finite Difference
Green’s function
Impulse response of a unit power source
Fourier heat equation
Symbol | Description
 | Density
 | Specific heat
 | Temperature
 | Ambient Temperature
 | Conductivity
 | Heat Generation Rate
 | 2D Convolution
Symbol | Description
 | Density
 | Specific heat
 | Temperature
 | Ambient Temperature
 | Conductivity
 | Heat Generation Rate
 | 2D Convolution

## Slide 4: Thermal modeling Approach
Green’s function
Final temperature profile
Analytically
Geometry
Power profile

## Slide 5: OVERVIEW
The standard thermal modeling approach involves solving the Fourier heat equation
At the nanoscale level, the Fourier equation fails to hold because of quantum effects
  The Boltzmann transport equation (BTE) needs to be solved
  Computationally expensive
We propose a hybrid Fourier-Boltzmann framework to model chip level as well as nanoscale effects
  Balance speed and accuracy

## Slide 6: FOURIER-BTE COMPARISON
We compare the BTE steady state solution against the Fourier steady state solution
Maximum error of 53% using the Fourier solution, with respect to the BTE solution.
Comparison of Fourier and BTE solutions
Ignoring nanoscale effects leads to large errors

## Slide 7: NANOTHERM
We have developed an analytical Fourier-Boltzmann framework to model a full chip by combining architectural level and nanoscale level thermal effects. We call our tool, NanoTherm
Overview of the algorithm

## Slide 8: NANOSCALE THERMAL MODELING
Chip level
thermal
simulation
Nanoscale level
thermal simulation
Combined chip level and nanoscale level

## Slide 9: ARCHITECTURAL THERMAL SIMULATIONS: SYSTEM LAYOUT
System layout
Approximated model

## Slide 10: ARCHITECTURAL THERMAL SIMULATIONS: SYMMETRIC THERMAL DISTRIBUTION
Fourier heat equation:
Circular power
source
Symmetric temperature distribution
Symmetry in thermal distribution:

## Slide 11: Theoretical Tool Used: Hankel Transform
A 1D Hankel transform is equivalent to a 2D Fourier transform of an isotropic function in polar coordinates.
Hankel transform of a radially symmetric function is given by:
Symbol List | 
 | Radially symmetric function in polar co-ordinates
r | Radial distance
Jo | Zero order Bessel function of first kind
 | Hankel domain variable
ˉˉ | Hankel Transform
Symbol List | 
 | Radially symmetric function in polar co-ordinates
r | Radial distance
Jo | Zero order Bessel function of first kind
 | Hankel domain variable
ˉˉ | Hankel Transform

## Slide 12: ARCHITECTURAL THERMAL SIMULATIONS
Fourier heat equation:
Symbol List | 
 | Layer number
ρ | Density
c | Specific heat
k | Thermal conductivity
Φ | Tl – Ta
Φ | Laplace transform
 | Hankel transform
σ | Hankel domain variable
s | Laplace domain variable
Symbol List | 
 | Layer number
 | Density
 | Specific heat
 | Thermal conductivity
Φ | Tl – Ta
Φ | Laplace transform
 | Hankel transform
σ | Hankel domain variable
s | Laplace domain variable
This is a standard ordinary differential equation
Zero order Bessel differential operator
Time derivative
Using the Hankel transform:
Using the Laplace transform:

## Slide 13: ARCHITECTURAL THERMAL SIMULATIONS
General solution:
For a particular solution, we take the Hankel transform of the boundary conditions and apply them to the obtained general solution.
We obtain a set of four linear equations, and we solve them to obtain the coefficients.
Symbol List | 
ro | Radius of the heat source
Jo, J1 | Zero and first order Bessel function of first kind
 | for silicon and 2 for HS
b | Thickness of heat spreader
δ | Thickness of silicon chip
Symbol List | 
ro | Radius of the heat source
Jo, J1 | Zero and first order Bessel function of first kind
b | Thickness of heat spreader
δ | Thickness of silicon chip

## Slide 14: ARCHITECTURAL THERMAL SIMULATIONS
Steady state analytical solution:
Transient analytical solution:
Symbol List | 
Kl | Heat conductivity
ρl | Density
c | Specific heat
σ | Hankel domain variable
s | Laplace domain variable
 | Hankel transform
ro | Radius of heat source
Jo, J1 | Zero and first order Bessel func. of first kind
l | 1 for silicon and 2 for HS
b | Thickness of HS
δ | Thickness of silicon chip
Symbol List | 
Kl | Heat conductivity
ρl | Density
c | Specific heat
σ | Hankel domain variable
s | Laplace domain variable
 | Hankel transform
ro | Radius of heat source
Jo, J1 | Zero and first order Bessel func. of first kind
l | 1 for silicon and 2 for HS
b | Thickness of HS
δ | Thickness of silicon chip
σ

## Slide 15: NANOSCALE THERMAL SIMULATIONS: BTE
Gray Boltzmann transport equation:
Gray BTE is frequency independent. It assumes that all phonons have the same relaxation time and group velocity.
  Reduction in complexity
Boltzmann transport equation (BTE) under Bhatnagar–Gross–Krook approximation:
Symbol List | 
Q | Volumetric heat generation
C | Specific heat
τeff | Effective relaxation time constant
eω | Frequency dependent energy density distribution function per unit solid angle
e | Energy density distribution function per unit solid angle
eo | Avg energy density distribution function
vg | Group velocity
 | Direction of momentum
Symbol List | 
Q | Volumetric heat generation
C | Specific heat
τeff | Effective relaxation time constant
eω | Frequency dependent energy density distribution function per unit solid angle
e | Energy density distribution function per unit solid angle
eo | Avg energy density distribution function
vg | Group velocity
 | Direction of momentum

## Slide 16: NANOSCALE THERMAL SIMULATIONS
Gray Boltzmann transport equation:
Symbol List | 
Q | Volumetric heat generation
ξx,ξy,ξz | Spatial frequencies(x, y, z)
ξ | √ ξ2x ξ2y ξ2z
η | Temporal frequency
~ | Represents Fourier transform
Λ | Mean free path
Using the Fourier transform:

## Slide 17: NANOSCALE THERMAL SIMULATIONS

## Slide 18: NANOSCALE THERMAL SIMULATIONS

## Slide 19: NANOSCALE THERMAL SIMULATIONS
Steady state analytical solution:
Transient analytical solution:
Temperature profile can be obtained using simple convolution.
Symbol List | 
Q | Volumetric heat generation
ξx,ξy,ξz | Spatial frequencies(x, y, z)
ξ | √ ξ2x ξ2y ξ2z
η | Temporal frequency
~ | Represents Fourier transform
Λ | Mean free path

## Slide 20: CIRCLE TO SQUARE MAPPING
Sampling points
Smallest grid
The obtained solution is for a circular source but the floorplan elements in real chips/SoCs are rectangular
We need to map circular point sources to rectangular/square sources
We sample our Green’s function solution at sample points obtained by discretizing the chip into a grid
Equiarea circle
Sampling points

## Slide 21: EDGE and CORNER EFFECTS
Temperature suddenly drops to zero

## Slide 22: Extended Green’s function
2x size of the chip
Extended Green’s function

## Slide 23: Full chip temperature Calculation
Make the power matrix 2 times the original size by zero padding
Folding
Final temperature

## Slide 24: System Details
All simulations were done on a Dell OptiPlex 3010 desktop
Dell OptiPlex 3010 specification:
  Intel(R) Core(TM) i7-3770S CPU @ 3.10GHz
  8 GB DDR3 RAM
  Operating system: Ubuntu 18.04

## Slide 25: NANOTHERM RESULTS: CIRCLE TO SQUARE MAPPING
We compare the analytical model against a commercial CFD solver COMSOL.
Error < 3%
Steady state Green’s function
Speedup over COMSOL: 3719X

## Slide 26: NANOTHERM RESULTS: FOURIER EQUATION
Full chip steady state
Error < 2 %
Case 1:
Case 2:
Error < 3%
Power profile
Thermal profile
Speedup over
COMSOL: 3719X

## Slide 27: NANOTHERM RESULTS: FOURIER EQUATION
Case 3 - Alpha21264 : Full chip steady state
Error = 3%
Power profile
Thermal profile
Speedup over
COMSOL: 3719X

## Slide 28: NANOTHERM RESULTS: FOURIER EQUATION
Case 4 - Intel Gainestown dual core : Full chip steady state
Error < 3%
Power profile
Thermal profile
L3
LSU
L2
EU
IFU
MMU
RU
LSU
L2
EU
IFU
MMU
RU
Speedup over
COMSOL: 3719X

## Slide 29: NANOTHERM RESULTS: FOURIER EQUATION
We compare the analytical model against a commercial CFD solver COMSOL.
Maximum error for transient simulation: 1%
Transient Step Response
Speedup over
COMSOL: 724X

## Slide 30: NANOTHERM RESULTS: FOURIER EQUATION
Full chip transient:
Error < 2%
Power profile
Thermal profile
at t = 0.01 ms
Thermal profile
at t = 2 ms
Thermal profile
at t = 4 ms

## Slide 31: NANOSCALE RESULTS: BTE
We performed the simulation for a 60nm*45nm*20nm channel FET
We compare the analytical model against ThermalScope.
Steady state
Error = 2%
Speedup over
ThermalScope: 668X

## Slide 32: NANOSCALE RESULTS: BTE
We performed the simulation for a 60nm*45nm*20nm channel FET
Transient
Error = 3%
Speedup over
ThermalScope: 73X

## Slide 33: NANOSCALE RESULTS: SUMMARY
Simulator | Fourier heat equation |  | BTE | 
 | Steady | Transient | Steady | Transient
Hotspot | 1s | 36s | - | -
3DICE | 1.36s | 1.77s | - | -
COMSOL | 305s | 3005s | - | -
ThermalScope | 11.1s | 35.55s | 2206s | 2888s
NanoTherm | 0.082s | 4.15s | 3.3s | 39.5s

## Slide 34: COMPARISON OF EXECUTION TIME FOR FOURIER SOLUTION
Chart: Comparison of Execution Time (Fourier)
| Steady | Transient
Hotspot | 1 | 36
3DICE | 1.36 | 1.77
ThermalScope | 11.1 | 35.55
COMSOL | 305 | 3005
NanoTherm | 0.082 | 4.15
305s
3005s

## Slide 35: COMPARISON OF EXECUTION TIME FOR BTE SOLUTION
Chart: Comparison of Execution Time (BTE)
| ThermalScope | NanoTherm
Steady | 2206 | 3.3
Transient | 2888 | 39.5
2206s
2888s

## Slide 36: Conclusion
We have developed a full chip thermal estimation method incorporating nanoscale effects.
In this work we have successfully computed the closed form solution for the Fourier and BTE equations in the transform domain.​
The solution was obtained for all settings: steady-state and transient​
The analytical solution is much faster than FEM-based solvers like COMSOL, ThermalScope, HotSpot and 3D-ICE

## Slide 37
37